## Slide 1: Multi-hop Relaying with Optimal Decode-and-Forward Transmission Rate and Self-Immunity to Mutual Interference among Wireless Nodes
Xiaohua Li and Jeong Kyun Lee
Department of Electrical and Computer Engineering
State University of New York at Binghamton
{xli,jlee54}@binghamton.edu

## Slide 2: Major contributions
Develop efficient algorithm to construct optimal multi-hop path in arbitrarily large wireless networks
  Interference immune phenomenon: Multi-hop relaying as if no mutual interference. Take the benefits of broadcasting without the problem of mutual interference
  Efficient Dijkstra-like algorithm: Select multi-hop relays for optimal source-destination rate with complexity

## Slide 3: 1. Introduction
Multi-hop networking problem:
  Find optimal hop count, select optimal relays, determine optimal source-destination rate
  Wired networks:
    Dijkstra’s algorithm (shortest path, widest path)
  Wireless networks: an open challenge
    Challenge of mutual interference, broadcasting

## Slide 4: Existing work for this wireless information flow problem
Exhaustive search based on max-flow min-cut theorem  complexity too high
Capacity scaling  asymptotic results at only
Relay/cooperative communication  for small networks (a few fixed nodes or hops only)
Hop count and multi-hop relay optimization  has been studied in a linear network only

## Slide 5: Objective: Algorithmic Approach
Algorithmic approach for this problem
  Develop new multi-hop relay selection algorithm to construct optimal multi-hop path
  Efficient for wireless networks with arbitrary size
  Optimal in terms of decode-and-forward rate
Based on an interesting phenomenon of wireless networks: interference immunity
  A large class of multi-hop wireless operations can be conducted as if there is no mutual interference

## Slide 6: 2. System model
Wireless network with random nodes
  Source node , destination node , and relay candidate nodes
  Need to select relays to construct rate-optimal multi-hop path from source to destination

## Slide 7: Relaying strategy
Assume causal full-duplex (FD) decode-and-forward (DF) relays
  A relay can transmit simultaneously a packet while receiving another packet
  DF is popular in practical or large multi-hop wireless networks
  FD is optimal theoretically, promising practically
  Causality: relay can transmit packets received/decoded during past slots only

## Slide 8: Slotted multi-hop packet forward scheme
One packet per slot: A packet reaches the destination node in each slot

## Slide 9: Signal model
Relay receives all other relays’ broadcasted signals
    Signals transmitted by relays in its preceding hops
    Signals transmitted by itself
    Signals transmitted by relays in its subsequent hops

## Slide 10: Assumptions on signal model
Each relay has a power limit:
  Need to optimize relaying power
Each relay has AWGN with power
Instantaneous flat fading channel:
Transmitted signal has unit power:
Channels coefficients and re-encoding rules are public knowledge

## Slide 11: 3. Interference immune phenomenon
Exploit FD & known packets
  Relay can subtract self-interference and interference from relays in subsequent hops
  Received signal consists of information from preceding relays only
Key challenge: How to mitigate interference from preceding relays?
  Answer: Exploit multiple repeated transmissions in multi-hop operations

## Slide 12: Exploit multiple repeated transmission of the same packet
Each packet is transmitted once by each relay
Full knowledge of relay on a packet: signals received in past slots

## Slide 13: Successive interference cancellation
To decode packet , relay uses all its signals received in past slots
  Apply SIC to remove decoded packets
  SINR of detecting signal
    Still has interference from preceding relays

## Slide 14: Achieve immunity to mutual interference
With appropriate re-encoding, overall rate of relay is
  No mutual interference remains interference immune phenomenon
  Broadcasting of preceding relays is collected  enjoy benefits of broadcasting without suffering from mutual interference

## Slide 15: 4. Algorithmic approach for optimal multi-hop path construction
Define source-destination rate
Formulate optimal multi-hop path construction
  Find optimal hop count, relay node selection and relay power optimization for rate maximization
Like a water pipe, rate is limited by the minimum tunnel

## Slide 16: Unique properties due to interference immunity
Relays just use full relaying power
A relay always increases rates of its subsequent relays
A relay is not affected by its subsequent relays
Greedy algorithm: It is optimal to adopt greedily all relays with highest rate

## Slide 17: Dijkstra-like Algorithm

## Slide 18: Optimality and efficiency
Proposition 1:
  Algorithm 1 finds the optimal hop count and selects relays to achieve maximum transmission rate with computational complexity .
  With slight modification, this algorithm can find optimal paths from a source node to all other nodes under same overall complexity .
  Optimal paths share common relays

## Slide 19: Decode-and-forward rate
Proposition 2: For 3-node relay network, algorithm 1 gives the optimal DF rate
Proposition 3: Single relay in each hop is optimal for DF relaying strategy

## Slide 20: 5. Simulations: Random network
Verified: optimality, efficiency, capacity scaling .

## Slide 21: A regular grid network: in fixed area or with fixed node density
Compare optimal DF rate with practically achieved rates.

## Slide 22: 6. Conclusions
Interference immune phenomenon:
  SIC+Encoding makes full-duplex decode-and-forward relays interference-free
Multi-hop path construction for optimal DF rate
  Exploit multi-hop broadcasting without suffering from mutual interference
Dijkstra-like algorithm for wireless networks
  Find optimal hop count, optimal relays, to maximize DF rate
  Efficient for arbitrarily large wireless networks